Ultra-long Standby wireless GPS (H505)

(not rechargeable battery)

Product Display:

# One. Products Description

# Ultra-long standby gps tracker use military disposable batteries. It’s sleep mode when the device is turn off, when arrived transmitting data time, the device automatically wake up and start locating and send data. Meantime, it support base station location, to obtain the approximate location of device when no GPS signal.

# Two. Function

1.modify the reporting interval mode: SMS, GPRS, data lines, equipment must wake up , then it can modify the reporting interval time via SMS or GPRS .

2. the key trigger wake, easy installation and commissioning.

3.optional magnetic (optional)

4. IP67 waterproof design, effectively prevent the device from water.

5.using military disposable batteries, ensure long-term use.

6. Work schedule:

| Standby time | 15 days | 4 month | 14month | 26month | 4year |
| --- | --- | --- | --- | --- | --- |
| Positioning interval time | 5min/time | 1h/time | 6h/time | 12h/time | 24h/time |

According to a particular environmental tests for above work schedule time, in a different working environment will be some deviation.

# There.LED Indications

Device has two lights, a red light, a blue light. Blue light flashing means searching signals. Red light flashing means sending messages or data. The two lights only work trigger it off with a single button, automatic wake-up time  will not work.

# Four. Set Up

1.Modify IP address and port

modify the IP and port via SMS, device will handle the message when GSM module wake up.  So it can send message advance, when GMS module wake up, After receiving message, will handle it automatically.

Send SMS to the unit as below format:

ip203.195.171.42port9903

Explain: IP :command, 203.195.171.42 is server IP address.

Port: server port. 9903 is port value.

2. set Device ID

Send SMS to set device ID as below format:

number13612341234

Explain: number is command

13612341234 is device ID. Device ID should be 11 digtial

- Modify device password

Device default password is 123456, it can change via SMS. Format as below:

password123456 138138

Explain: Password is command

123456 is device initial password

138138 is device new password

Password must be 6 digital

4.Set interval time

Device default interval time is 24h per time. It can change interval time by SMS. SMS format:

p123456at5start0900

Explain: P is password mark

123456 is device password

At is auto track mark

5 is interval time, unit is minute, means every 5 min report a data.( digital 5 can change to 1440, 1440 means 24h report a data. Min interval time is 5 minute. Max interval time is 24h.

Start: start remark. 0900 means 9:00 in the morning start to report data. 1830 means 18:30 in the afternoon start to report data.

5.Set APN

report In order to send GPS data to IP address, you still must set mobile network Access Point Name (APN). If you don’t know the APN, you can consult local network service .The format of setting APN as below:

APN123456 cmnet

Explain: APN is command

123456 is device default password

After password 123456, there is a space.

CMNET is apn value.( China mobile)

# 5. Installation Notes

1. Put the SIM card in fixed place, check carefully if it’s insert well to prevent SIM are loose or fall off, resulting in abnormal working.

2. The card is installed, plug in the battery transposons, check if is seated.

3. Battery inserted, you can press the button to check whether the SIM card can work properly.

4. GPS antenna shoul be face up to ensure GPS signal reception

# 6. Parameters

| Content | Specs |
| --- | --- |
| GSM Module | SIM800C |
| GPS Chip | MT3337 |
| GPS Sensitivity | -160dBm |
| GPS Accuracy | 3 – 30m |
| Size | 83* 58 * 34(mm) |
| Weight | 0.16KG |
| Operation Temp. | -20°C to +70°C |
| Storage Temp. | -40°C to +85°C |
| Humidity | 5 - 95% RH |
| Work Voltage | DC 3.6V |
| Battery Capacity | 6600mAh（Disposable batteries） |
| Standby work currents | 2uA |

Shenzhen Legevo Technology Co.,LTD

Tel: 86-755-25911595-605

Fax: 86-755-25911595-608

Email:sales@legevo.com

Web:www.legevo.com

Add: Rm 811-815, 523 building, Bagua 2nd Road,Bagualing, Futian Dist,Shen Zhen, Guang Dong ,China